## Slide 1: Vegetation Index Focus Area
Tomoaki Miura & Else Swinnen
Activity Summary and Strategic Plan for 2019-2021

## Slide 2: Two Vegetation Index Focus Area Workshops
1st Workshop:
VI & LSP Workshop Fort Collins, CO, USA, 9-10 November 2016
2nd Workshop:
VI Workshop Washington, D.C., USA, 12 December 2018

## Slide 3: Recommendations Established at the Workshops
CEOS recommends that the validation document of a VI product include:
  Product QA information
  Uncertainty information obtained via validation (NIST-traceability)
  Product inter-comparison results

## Slide 4: Recommendations Established at the Workshops
CEOS identifies three components of VI validation:
  Uncertainty of VIs in their units (e.g., DNDVI)
  VI sensitivity to vegetation biophysical/physiological conditions (e.g., LSP, GPP, LAI)
  Long-term stability information of VI time series data
Recommended validation data sources (systematic-opportunistic):
  AERONET-based surface reflectance data
  NEON airborne hyperspectral data
  Drone-observational reflectance data
  Near-surface remote sensing data: PhenoCam
  Field spectrometer time series data: PEN
  NPN phenology data
  FLUXNET data
  Time-lapse digital imagery: PhenoCam, Phenological Eyes Network (PEN)
  High resolution satellite data, given that they are validated against ground measurements
Adopted the “time series validation” approach as a standard VI validation methodology where validation focuses on validating the quality of VI time series data as to how well VI products capture seasonal evolution of vegetation

## Slide 5: Recommendations Discussed at the Workshops
Discussed that the focus of product inter-comparison was to characterize the differences and their spatial and temporal distribution
  Suggested measures
    Product completeness
    Spatial consistency
    Statistical consistency
    Temporal consistency
  Statistical metrics discussed included:
    RMSD (split into its systematic and unsystematic components)
    Mean Bias Error, Mean Absolute Error
    Precision or repeatability

## Slide 6: Strategic Plan for 2019-2021
Main Goal: generate the first draft of the VI best validation practices document