## Slide 1: Overview of NEON’s Airborne Observation Platform CEOS WGCV Land Product Validation Plenary
Tristan Goulden​
Science Lead​
Airborne Observation Platform (AOP)
Ian Crocker, Bridget Hass, Keith Krause, John Musinsky, Katherine Murphy, Alok Shrestha
​
National Ecological Observatory Network
A project sponsored by the National Science Foundation and proudly operated by Battelle

## Slide 2: Airborne Observation Platform (AOP)
Collects airborne remote sensing data
Covers ‘regional scale’ (min of 100 km2)
Data products generated at high spatial resolution (<=1 m2)
Waveform Lidar, Imaging Spectrometer and RGB camera

## Slide 4
Notes: NEON will provide data to inform these grand challenges by providing data collected by instruments located on our airborne platform, tower, in the soil and aquatic systems, and observations made both on land and in the water.

## Slide 5: AOP Payloads – three in total
NEON Imaging Spectrometer (NIS)
Lidar / Camera

## Slide 6: Waveform LiDAR Sensor
Active-source instrument
  1064 nm
Transmits laser pulses at up to 1000 kHz
Capable of recording multiple discrete returns per pulse
Provides structural information about the landscape

## Slide 7: NEON Imaging Spectrometer (NIS)
Images acquired in pushbroom configuration
  34 deg across-track
  1 mrad along-track
  1000m AGL = 1m2 resolution
Each 1 mrad pixel imaged light is spread into its component wavelengths 380 - 2510 nm
5nm spectral sampling interval with <7.5nm FWHM
Notes: We end up with hyperspectra data “cubes” of dimension x*y*# bands (usually 426). This provides rich information about the chemical properties of the vegetation we are flying over. We also make derived products from the hyperspectral data, such as indices or band ratios that indicate different properties (eg. NDVI – Normalized Difference Vegetation Index)

## Slide 8: Digital Camera Sensor
Commercial instrument delivered with Optech or Riegl lidar system: DiMAC D-8900 or PhaseOne iXA
Purpose
  Context for lidar and spectrometer
  Provides sub-meter sampling of scene @ 1000 m AGL
  High spatial accuracy

## Slide 9
2013 – 2020 AOP collections

## Slide 10
2021 AOP collections

## Slide 11: AOP Sampling Collection Requirements
Clear skies
Nominal AOP flying altitude = 1000 m AGL
  Driven by requirement to collect data at the scale of individual plants
Minimum 10 km by 10 km box
  Driven by requirement to collect regional scale area around NEON sites
Fly at peak ‘greenness’
  Driven by requirement for consistency between annual collections
Fly N-S lines when solar angles are above 40°

## Slide 12
HARV
Notes: Integrated data collection at 81 field sites distributed across 20 domains – or ecoregions – in the United States (including Puerto Rico, Alaska, and Hawaii)

## Slide 15: NEON AOP data products
Plot 192 - Mixed Blue and Live Oak
Spectrometer Orthrorectified at-Sensor Radiance
LiDAR Slant Range Waveform
Discrete Return LiDAR Point Cloud
Spectrometer Orthorectified Surface Directional Reflectance
High-resolution Orthorectified camera imagery
Canopy Water Content
Canopy Xanthophyll Cycle
Canopy Lignin
Canopy Nitrogen Vegetation Indices – Spectrometer
Albedo - Spectrometer
LAI - Spectrometer
fPAR - Spectrometer
Total Biomass Map - Spectrometer
Spectrometer Orthorectified Surface Directional Reflectance
High-resolution Orthorectified camera imagery mosaic
Albedo - Spectrometer
LAI - Spectrometer
fPAR - Spectrometer
Total Biomass Map - Spectrometer
Canopy Nitrogen
Canopy Water Content
Canopy Xanthophyll Cycle
Canopy Lignin
Vegetation Indices - Spectrometer
Ecosystem Structure
Elevation - LiDAR
Slope and Aspect - LiDAR
Level 1
Level 2
Level 3
Raw data to
physical units
Derived products
e.g. indices
Derived product mosaics
ATBDs (Algorithm Theoretical Basis Documents) describing the process for data product creation
Temporarily Suspended Products

## Slide 16
Visible

## Slide 17
RGB Image
False Color Image (NIR GB)

## Slide 18
DSM
DSM

## Slide 19
DSM
DTM

## Slide 20
DSM
> 25 m
0 m
DTM
CHM

## Slide 21
RGB
NDVI
Burned area Live vegetation

## Slide 22: Data Interoperability with EOS
D05 – UNDE
flight box
DESIS collection 20190608
Landsat 8 - 20200913
Sentinel 2A - 20200913
Include ground field spectrometer measurements

## Slide 23: Radiometric Calibration
Radiometric Calibration
NIST bulb / spectralon panel
ASD as transfer radiometer
Integrating sphere
NIS
Integrating
Sphere
NIST bulb
Calibrated Spectralon Panel

## Slide 24: Vicarious Calibration
Performed at Table Mountain, Railroad Valley
Measure calibration tarps, gravel road and vegetation with ASD coincident with overpass
Compare at-sensor radiance observed from NIS against MODTRAN simulation

## Slide 25: Vicarious Calibration
48%
3%

## Slide 26: Data Challenges
Currently hold ~100s TB of data products, >100 TB intermediate files
Anticipate collecting ~ 100 TB per year (raw and processed)
At-sensor radiance, waveform LiDAR, reflectance (L1) require majority of the storage space (80%)
Getting data to our users
Harmonization of data
Educating users on data use and uncertainty

## Slide 27: AOP as an Assignable Asset

## Slide 28: AOP Assignable Asset Research